## Slide 1: CSC358: Principles of Computer Networks
Lecture 2-Part 1: Network Sharing
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: Today’s Outline
Part 1: How is a network shared?
  Circuit switching
  Packet switching
    Statistical Multiplexing
Parts 2-4: Physical/Link layer
  Different types of media
  Encoding bits with signals
  Framing

## Slide 3: Circuit Switching
It’s the method used used to be used by the telephone network.
A call has three phases:
  Establish circuit from end-to-end (“dialing”),
  Communicate,
  Close circuit (“tear down”).
Originally, a circuit was an end-to-end physical wire.
Nowadays Previously, a circuit was like a virtual private wire:
  each call has its own private, guaranteed data rate from end-to-end.
A
B
Source
Destination

## Slide 4: Circuit Switching
Reservation establishes a “circuit” within a switch
switch
src
dst

## Slide 5
Source
“Caller”
Central
Office
“C.O.”
Destination
“Callee”
Central
Office
“C.O.”
Trunk
Exchange
Each phone call is allocated 64kb/s. So, a 10Gb/s trunk line can carry about 156,000 calls.
Circuit Switching – Telephone Network

## Slide 6: Timing in Circuit Switching
Data
time
Circuit establishment
Data transfer
Circuit teardown

## Slide 7: Poor Efficiency in Circuit Switching
The circuit is mostly idle due to traffic bursts
time
Circuit establishment
Data transfer
Circuit teardown

## Slide 8: Poor Efficiency in Circuit Switching
The circuit is used for a short amount of time
Information
time

## Slide 9: Circuit switching doesn’t “route around trouble”
Once a circuit is established, all data follows that fixed path.
If a problem arises, the communication is disrupted because the circuit cannot dynamically reroute around the issue.
  circuit-switched networks lack mechanisms to automatically find alternative paths to bypass the trouble.
A
B

## Slide 10: Circuit Switching, Pros and Cons
Pros:
  Predictable performance
  Once circuit is established, it provides simple/fast switching
Cons:
  Complexity of circuit setup/teardown
  Inefficient when traffic is bursty
  Circuit setup adds delay
  Switch fails --> its circuit(s) fails

## Slide 11: Packet Switching
It’s the method used by the Internet
Each packet is individually routed,
  using the router’s local routing table
The routers maintain no per-flow state
Different packets with the same source and destination address may take different paths
Several packets may arrive for the same output link at the same time,
  Therefore, a packet switch has buffers

## Slide 12: Packet Switching
A
R1
R2
R4
R3
B
Source
Destination
C
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 13: Packet Switching
A
R1
R2
R4
R3
B
Source
Destination
C
With buffers to absorb transient overloads
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 14
R1
Link 1
Link 2
Link 3
Link 4
Link 1, ingress
Link 1, egress
Link 2, ingress
Link 2, egress
Link 3, ingress
Link 3, egress
Link 4, ingress
Link 4, egress
Choose
Egress
Choose
Egress
Choose
Egress
Choose
Egress
“4”
“4”
Packet Switching – Simple Switch Model

## Slide 15
time
Arrival rate
One flow
Two flows
Average rate
Many flows
Average rates of: 1, 2, 10, 100, 1000 flows.
Statistical Multiplexing – Basic Idea
Network traffic is bursty, i.e., the rate changes frequently
Peaks from independent flows generally occur at different times
Conclusion: The more flows we have, the smoother the aggregate traffic.
time
time

## Slide 16
B
A
time
time
Packet arrival Rate
C
C
A
C
B
C
Statistical Multiplexing Gain (SMG)
Packet arrival Rate
Notes: Statistical multiplexing
Important if traffic is bursty
Less expensive
Contention requires buffering
Variable delay => no QoS guarantees

## Slide 17
A
B
R
2C
R < 2C
A+B
time
Statistical Multiplexing Gain (SMG)
Packet arrival Rate
B
A
Statistical multiplexing gain = 2C/R
Other possible definitions of SMG:
  The ratio of rates that give rise to a particular queue occupancy,
  The ratio of buffer size that give rise to a particular loss probability.
Notes: Statistical multiplexing
Important if traffic is bursty
Less expensive
Contention requires buffering
Variable delay => no QoS guarantees

## Slide 18: Why Packet Switching in The Internet
Efficient use of expensive links:
  The links are assumed to be expensive and scarce.
  Packet switching allows many, bursty flows to share the same link efficiently.
  “Circuit switching is rarely used for data networks, ... because of very inefficient use of the links” - Gallager
Resilience to failure of links & routers:
  “For high reliability, ... [the Internet] was to be a datagram subnet, so if some lines and [routers] were destroyed, messages could be … rerouted” - Tanenbaum

## Slide 19: Questions for the rest of the semester
Is layering the best approach?
  Simplifies design
  Yet, limited and inflexible
Best effort service
  Made the rapid growth of the Internet possible
  Makes providing any guarantees very difficult
Packet switching
  Enables statistical multiplexing
  We need extremely fast routers
Routing: How does a router know which output port to send the packet to?