## Slide 1: CSC358: Principles of Computer Networks
Lecture 2-Part 3: Encoding
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: Today’s Outline
Part 1: How is a network shared?
  Circuit switching
  Packet switching
    Statistical Multiplexing
Physical/Link layer
  Part 2: Different types of media
  Part 3: Encoding bits with signals
  Part 4: Framing

## Slide 3: So Far …
We saw how electromagnetic signals travel through different media
Next, we’ll see how digital data is transformed into electromagnetic signal, i.e., Encoding
Image credit: GEARit: https://www.gearit.com/blogs/news/ethernet-cable-wiring-diagram
Image credit: www.techtarget.com
Core glass
Cladding
Jacket
Core glass
Cladding
Jacket
Single-mode Fiber
Multi-mode Fiber

## Slide 4: Encoding Bits with Signals
Encoding/Decoding:
  Generate analog waveform (e.g., voltage) from digital data at the transmitter
  Recover the digital data from analog waveform at the receiver
In this course, we study 4 simple Encoding techniques
  NRZ
  NRZI
  Manchester
  4B/5B
Signals travel between signaling components; bits flow between adaptors
An Example of How Digital Data can be Encoded as Analog Waveform
Digital Data:
Analog Waveform:

## Slide 5: NRZ Encoding
1 as high, 0 as low!
  Called Non-return to Zero (NRZ)
Low is not necessarily 0V. For example, it could be -1V.
For example:
  Digital data to be transmitted: 001010110
  Use the clock cycle to generate analog waveform
    Clock is an internal signal that alternates from low to high, a low/high pair is considered as one clock cycle
0
0
1
0
1
0
1
1
0
Encoded
Waveform
Clock
Transmitter generates analog waveform from digital data, using its clock
Received Waveform
Clock
Receiver generates digital data from the received (noisy) analog waveform, using its clock
0
0
1
0
1
0
1
1
0
Decoded data

## Slide 6: Issues with NRZ
Baseline Wander: Too many consecutive 0’s and 1’s makes detection difficult
  The receiver keeps an average of the signals it has seen so far
    Uses the average to distinguish between low and high signal
    When a signal is significantly lower than the average, it is 0, else it is 1
Bit Slip: if sender and receiver clocks are not perfectly aligned the receiver may lose track of bit boundaries over time.

## Slide 7: Non-return to Zero Inverted (NRZI) Encoding
Encode 1 with transition from current signal
Encode 0 by staying at same level
NRZI at least solves the issue with consecutive 1s
Also, it makes clock recovery a bit easier than NRZ
0
0
1
0
1
0
1
1
0
Clock
NRZI

## Slide 8: Manchester Encoding
Merges the clock with signal by transmitting X-OR of the NRZ encoded data and the clock
  For a 0 bit: send a low-to-high waveform
  For a 1 bit: send a high-to-low waveform
Benefits:
  Self-clocking: the embedded clock makes synchronization and clock recovery easier
  Resolves the issue with consecutive 0s and 1s
Disadvantage:
  Bandwidth inefficient:
    Compared to NRZ and NRZI, provides half bandwidth (in bps)
Low-to-high
waveform
High-to-low
waveform

## Slide 9: 4B/5B Encoding
Every 4 bits is first encoded as 5 bits. Then, the transformed digital data is transmitted with NRZI.
Carefully select 16 5-bit chips such that
  No more than one leading 0 and no more than two trailing 0s in each 5-bit
Hence, no pair of 5-bit codes results in more than three consecutive 0’s
* No need to memorize this table

## Slide 10: 4B/5B Encoding
Properties:
  Resolves consecutive 0s and 1s issue
  Provides better bandwidth compared to Manchester, but lower than NRZ and NRZI
  Since it uses NRZI, it weakly provides clock
  Recovery, but not as good as Manchester

## Slide 11: NRZ, NRZI, Manchester, 4B/5B Applications
Encoding Technique | Applications
NRZ | Legacy systems
NRZI | USB
Manchester | Ethernet (10BASE-T), RFID, IR Communication
4B/5B | Fast Ethernet (100BASE-TX, 1000BASE-SX), Fiber Channel