## Slide 1: CSC358: Principles of Computer Networks
Lecture 3-Part 2: Error Detection and Correction
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: Errors
Bit errors are introduced into frames
  Electrical interference and noises are inevitable
    They can cause some of the bits to be flipped in the frame we receive
    i.e., changing a bit of 0 into 1 or vice versa.
  We must be able to detect/correct when this occurs! Why?
    Otherwise, the received message could be garbled and useless
  Who needs to do it? (links, routers, OSs, or apps?)
    Links, routers, and OSs

## Slide 3: Error Detection and Correction
In this part, we’ll introduce two techniques:
  Error Detection Codes
  Error Correction Codes
Why do we need to implement these techniques?
  To detect or correct messages that are garbled during transmission.

## Slide 4: Error Detection and Correction
Which layer implements these techniques?
  The responsibility for doing this cuts across the different layers, namely Link, Network, and Transport Layer
Why not just the link layer?
  Error detection at link layer:
    can detect and possibly correct errors for data transmitted over a single link (e.g., between a device and a router or access point).
Wouldn’t that be enough?
  No. Error detection at link layer does not account for errors introduced beyond that specific link.
  Errors can be introduced at other points, too.
    in routers and switches (e.g., when storing packets in buffer or processing them),
    In end-hosts (e.g., during reassembly from receiver’s buffer),

## Slide 5: Outline
Error detection and correction
  (N,K) block coding
  Hamming distance
  Parity,
  2D-Parity
  Checksums,
  CRC, …

## Slide 6: Detection vs. Correction
Error detection mechanisms* allow errors to be recognized
  How? Add redundant data.
We want to be overcome errors.
Two strategies to correct errors:
  Use error detection codes. If error is detected, request retransmition, or Automatic Repeat reQuest (ARQ)
  Error correcting codes, or Forward Error Correction (FEC)
    How? Add redundant data. Similar idea to error correction codes, but more complicated.
    Error correction codes allow errors to be repaired, too.
* Also known as error detection codes or error detection scheme

## Slide 7: Detection vs. Correction, cont’d
Error Detection Codes:
  Requires smaller number of bits/overhead
  Requires less/simpler processing
  But require retransmission which increases the traffic in the network.
Error Correction Codes:
  Reduce the number of retransmissions.
  But need more bits/overhead and requires more/complex processing.

## Slide 8: Retransmissions vs. FEC
Question: Which one should we choose? Retransmissions or FEC?
  Depends on the type of error, cost of recovery, and application.
Example: Message with 1000 bits, bit error rate 0.001
  Case 1: random errors  FEC
  Case 2: bursts of 1000 errors  ARQ
  Case 3: real-time application (teleconference)  FEC
FEC tends to be most useful when
  (1) errors are quite probable, as they may be, for example, in a wireless environment, or
  (2) the cost of retransmission is too high, for example, because of the latency involved retransmitting a packet over a satellite link.

## Slide 9: A Naïve Coding Scheme: Copycat Coding Scheme
Let’s start by studying a naïve coding scheme. We call it Copycat
  Sender sends two copies. Receiver looks for differences.
Example:
  Sender:
    Assume we are asked to send 0110100.
    We send 00111100110000 instead.
  Receiver:
    On the receiving end, we compare 1st bit with 2nd bit, 3rd bit with 4th bit, etc.
    If we notice any difference between them, it means that there is an error.
    For instance:
      E.g. 1: if we receive 00111101110000, we know that 7th or 8th bit was flipped.
        i.e., we detected error.
      E.g. 2: 00111100110000, we do not detect any error and return 0110100 as the sent message.

## Slide 10: Copycat Coding Scheme
Can Copycat detect any single bit of error?
  The answer is Yes. Why? We must prove it for any single bit of error.
Proof:
  On the sender’s side:
    Assume any arbitrary message. Let denote the size of the message.
    Sender sends bits as described in the previous slide.
  Single bit error along the path:
    Assume any arbitrary . Assume that just the bit is flipped in the received mesage.
  On the receiver’s side:
    Receiver compares 1st bit with 2nd bit, 3rd bit with 4th bit, etc.
    Thus, it compares the bit with its corresponding pair,
      i.e., th or th bit depending on being odd or even.
    Note that in the message sent by sender, bit and its pair are the same
    Since the bit was flipped while its pair was not, these two bits are different.
    Thus, the receiver notes this difference and detects error.

## Slide 11: Copycat Coding Scheme
Can Copycat detect any two bits of error?
  The answer is No. Why? It suffice to create a counter example in which two bits of flipped but the receiver does not detect error.
Proof:
  On the sender’s side:
    Assume message 11. Sender sends 1111.
  Two bits of error along the path:
    Assume that the and 2nd bit are flipped in the message received by the receiver.
  On the receiver’s side:
    Receiver receives 0011.
    Receiver compares 1st bit with 2nd bit, and 3rd bit with 4th bit.
    The receiver does not see any difference between each pair of bits.
    Thus, it does not detect any error and returns 01 as the sent message,
      It failed to detect the error.

## Slide 12: Copycat Coding Scheme Properties
What is the maximum number of flip of bits that Copycat is guaranteed to detect?  1
What is the overhead of Copycat?  100%
Question: Can we do any better? Catching more kinds of errors with less overhead?
Answer: Yes – stronger protection with fewer bits is possible
  But we can’t catch all inadvertent errors, nor malicious ones
We will look at basic block codes
  K bits in, N bits out is a (N, K) block code.
  k-information bits and (n-k) redundant error detection/correction bits.
  They are simple, memoryless mapping

## Slide 13: Outline
Error detection and correction
  (N,K) block coding
  Hamming distance
  Parity,
  2D-Parity
  Checksums,
  CRC, …

## Slide 14: (N,K) Block Coding
A (N,K) block coding scheme is a mapping function that
  It maps the set of possible K-bit messages
  onto the set of N-bit codewords,
  i.e.,
Example:
  Consider this (3,2) coding scheme 
  Assume message is 000111.
  What will be sent by this coding scheme?
A good mapping function makes it easy to detect errors among the resulting codes.
00
01
11
10
010
110
111
000
The set of 2-bit messages
The set of 3-bit codewords

## Slide 15: Copycat as (N,K) Block Coding
Example: Consider the Copycat coding scheme. Can you represent it as a (N,K) block coding scheme?
  What are N and K? N=2, K=1
  What is the mapping function?
1
0
11
00
The set of messages
The set of codewords

## Slide 16: Outline
Error detection and correction
  (N,K) block coding
  Hamming distance
  Parity,
  2D-Parity
  Checksums,
  CRC, …

## Slide 17: The Hamming Distance
The Hamming distance of two codewords:
  The number of bits that are different between two codewords
  e.g., HD(00001010, 01000110) = 3
The Hamming distance of a coding scheme:
  Minimum HD between any pair of mapped codewords of that coding scheme
Example: Consider a (3, 2) coding scheme with this mapping function
  What is this coding scheme’s Hamming distance?
    1
00
01
11
10
010
110
111
000

## Slide 18: The Hamming Distance, cont’d
Let be the Hamming distance of a coding scheme:
  The coding scheme can detect up to any bits of error. Why?
    How? if what received is not any of the codewords, you detect error
  Upon detecting an error, set the closest codeword to be the corrected version. This approach can correct up to any bits of error. Why?
Set of Codewords

## Slide 19: Next Week
Error detection and correction
  (N,K) block coding
  Hamming distance
  Parity,
  2D-Parity
  Checksums,
  CRC, …