## Slide 1: CSC358: Principles of Computer Networks
Lecture 5 – Part 2: Switched LANs
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: So Far …
So far:
  Network Interface Cards (NICs) send frame
  They have an “address”:
    MAC (Medium Access Control) address
      48 bits
      Assigned by manufacturer
      permanently hard-coded (“burned in”) on a device
    Nodes write their own MAC address and next hop MAC address as the source and destination MAC address in L2 header
  We saw how shared Ethernet, e.g., 10BASE5 works
Today:
  Interconnecting LANs
    Interconnect in Physical Layer
    Interconnect in Link Layer
  Why Are Modern Ethernet “Switched”?
  Cut-through switching
  Self-learning switches
  Spanning tree

## Slide 3: Interconnecting LANs
How to interconnect several LANs
  Technology:
    Physical Layer: Repeaters and Hubs
    Data Link Layer: Bridges and Switches
Repeater
Hub
Bridge
Switch

## Slide 4: Today
Interconnecting LANs
  Interconnect in Physical Layer
  Interconnect in Link Layer
  Why Are Modern Ethernet “Switched”?

## Slide 5: Interconnect LANs in L1: Repeater and Hub
Repeaters and hubs join LANs together in Physical Layer.
  Upon receiving a signal on a port, they send it out on all other ports.
They are dumb analog devices operating in L1.
  They don’t operate in L2. Thus, they don’t understand frames.
Repeater has two ports.
  Best used for connecting two bus segments
  Repeater transmits an amplified copy
Hubs have multiple ports
  Best used for connecting multiple nodes
  Hubs do not necessarily amplify the signal

## Slide 6: Limitations of Repeaters and Hubs
All connected nodes are in one large collision domain
  All hosts are competing for access to the same link
  Hence, they are said to be in the same collision domain
  Every bit is sent everywhere
  So, aggregate throughput is limited
Cannot support multiple LAN technologies
  Does not buffer or interpret frames
  So, can’t interconnect between different rates or formats
  e.g., 10 Mbps Ethernet and 100 Mbps Ethernet
Limitations on distances
  e.g., still cannot go beyond 2500 meters on Ethernet

## Slide 7: Today
Interconnecting LANs
  Interconnect in Physical Layer
  Interconnect in Link Layer
  Why Are Modern Ethernet “Switched”?

## Slide 8: Interconnecting LANs in L2: Bridges
Intelligent device that connects two or more bus segments at the link layer (L2)
  Extracts destination address from the frame
  Looks up the destination in its forwarding table
  Forwards the frame to the appropriate LAN segment
Each segment is its own collision domain
Nodes in the same segment cannot send frames simultaneously
Nodes on different segments can send frames simultaneously
host
host
host
host
host
host
host
host
host
host
host
host
Bridge

## Slide 9: Interconnecting LANs in L2: Switches
A switch is essentially the same as a bridge, though typically used to connect hosts, not LANs segments
  Each connection is a bidirectional point-to-point link
    Host has direct, full duplex* connection to the switch rather than a shared LAN connection
Like bridges, switches support concurrent communication
  In the figure below, Host A can talk to C, while B talks to D
* Full duplex: Both host and switch can send and receive data at the same time.

## Slide 10: Bridges and Switches – Traffic Isolation
Switch and bridge forward a frame only to the necessary port
  Lookup the destination MAC address of the frame in their forwarding table
Thus, segments become separate collision domains
  This allows longer distances, i.e., extended geographic span of the network
  This improves privacy by limiting the scope of frames
They apply carrier sense and collision detection
  Does not transmit when the link is busy.
  Applies exponential back-off after a collision
They can join segments that use different technologies (e.g., different transmission rate)

## Slide 11: Today
Interconnecting LANs
  Interconnect in Physical Layer
  Interconnect in Link Layer
  Why Are Modern Ethernet “Switched”?

## Slide 12: Why Are Modern Ethernet “Switched”?
Ethernet was invented as a broadcast technology
  Hosts share channel
  Each packet received by all attached hosts
  CSMA/CD for access control
Current Ethernets are “switched”
  bidirectional point-to-point link
Why Are Modern Ethernet “Switched”?

## Slide 13: Limits on Traditional Ethernet Scalability
In shared medium LANs, to successfully detect collisions,
  Need transmission time > 2 propagation delay
  Requires either very large frames (underutilization) or small scale.
  Example: consider 100 Mbps Ethernet
  Suppose minimum frame length: 512 bits (64 bytes)
    Transmission time = 5.12 sec
    Thus, propagation delay < 2.56 sec
    Length < 2.56 sec speed of light Length < 768m
  Cannot scale beyond 76.8m for 1Gbps and beyond 7.68m for 10Gbps
This is WHY modern Ethernet networks are “switched”

## Slide 14: Disadvantages Over Hubs/Repeaters
More expensive compared to hub/repeater
Delay in forwarding frames
  Bridge/switch must receive and parse the frame and perform a look-up to decide where to forward
  Storing and forwarding the packet introduces delay
  Solution: cut-through switching  We’ll study this in the next slide
Need to learn where to forward frames
  Bridge/switch needs to construct a forwarding table
    Ideally, this must be done without intervention from network administrators
  Solution: learning switches We’ll study this in the next part

## Slide 15: Store-and-forward vs. Cut-through Switching
Store-and-forward switching
Buffering a frame takes time
  Suppose L is the length of the frame and R is the transmission rate
  It takes L/R to receive the frame
This buffering delay can be a high fraction of total delay
  Propagation delay is small over short distances
  Thus, buffering delay is a large fraction of total delay
Cut-through switching
Starts transmitting as soon as possible
  Inspects the frame header and do the look-up in the forwarding table
  If outgoing link is idle, starts forwarding the frame
It allows overlapping transmissions
  Transmits the head of the packet via the outgoing link, while still receiving the tail via the incoming link