## Slide 1: CSC358: Principles of Computer Networks
Lecture 6 – Part 3: IP Packet Format
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: Today
IP Addressing
Subnetting
The IP Packet format
Packet Forwarding
Internet Control Message Protocol (ICMP)
Discovery protocols: ARP and DHCP
Turning names into addresses (DNS)

## Slide 3: IP Packet Structure
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits
32 bits
16 bits

## Slide 4: IP Packet Structure
Version field: The version number
  Tells us what other fields to expect, typically it is set to “4” for IPv4, or “6” for IPv6
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 5: IP Packet Structure
Header Length Field: The number of 32-bit (i.e., 4 byte) words in the header
  typically set to 5 (20 bytes header)
  Can be more when “IP options” are used.
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits
Counts in Words (i.e., in 4 bytes)

## Slide 6: IP Packet Structure
TOS Field: Allows different packets to be treated differently
  e.g., low delay for voice, high bandwidth for video
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 7: IP Packet Structure
Total Length Field: Number of bytes in the entire packet, with a maximum of 65 535 bytes
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits
Bytes
Counts in Bytes

## Slide 8: IP Packet Structure
Supports dividing a large IP packet into fragments, in case a link cannot handle a large IP packet
version | header length | Type of service (TOS) | Total Length |  |  | 
Identification |  |  | 0 | DF | MF | Fragment offset
Time to Live |  | Protocol | Header Checksum |  |  | 
Source IP Address |  |  |  |  |  | 
Destination IP Address |  |  |  |  |  | 
Options (if any) |  |  |  |  |  | 
Payload |  |  |  |  |  | 
4 bits
indicates the number of 8-byte data preceding or ahead of the fragment (e.g., if this field is set to 100, it means that 800 bytes of data precedes the data part of this fragment.
Always 0
Don't Fragment bit
If set, this packet should not be fragmented.
More Fragments bit
is set on all fragmented packets except the last one

## Slide 9: IP Fragmentation
Problem:
  A router may receive a packet larger than the maximum transmission unit (MTU) of the outgoing link.
A
Ethernet
MTU=1500 bytes
MTU=1500 bytes
B
Source
Destination
MTU<1500 bytes
R1
R2

## Slide 10: IP Fragmentation, cont’d
Solution:
  R1 fragments the IP datagram into multiple, self-contained datagrams
Data
HDR (ID=x)
Data
HDR (ID=x)
Data
HDR (ID=x)
Data
HDR (ID=x)
Offset>0
More Frag=0
Offset=0
More Frag=1
Offset>0
More Frag=1

## Slide 11: IP Fragmentation, cont’d
Fragments are re-assembled by the destination host
  not by intermediate routers
To avoid fragmentation, hosts commonly use path MTU discovery to find the smallest MTU along the path.
Path MTU discovery involves sending various size datagrams until they do not require fragmentation along the path.

## Slide 12: IP Fragmentation, cont’d
Most links use MTU1500 bytes today.
Try:
wolf:~$ traceroute -I -F uwaterloo.ca 1501
traceroute to uwaterloo.ca (151.101.66.133), 30 hops max, 1501 byte packets
1 * 0.030 ms !F-1500 * *
Since DF is set in IP header, routers send “ICMP” error message indicating fragmentation is required
  which is shown as “!F-1500” in the traceroute result
Bonus: Can you find a destination for which the path MTU < 1500 bytes?

## Slide 13: IP Packet Structure
Used to identify packets trapped in a loop, and eventually discard them
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits
Hop count

## Slide 14: IP Packet Structure
The upper-level protocol carried in the packet
  e.g., “6” for TCP, “17” for UDP, “1” for ICMP
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 15: IP Packet Structure
Header Internet Checksum
  Does not protect the payload
  If header bits are corrupted, checksum won’t match, and receiver discards corrupted packets
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 

## Slide 16: IP Packet Structure
Uniquely identify the source and destination host
  Why do we need source IP?
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits