## Slide 1: CSC358: Principles of Computer Networks
Lecture 6 – Part 4: Forwarding and Data Plane
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: Today
IP Addressing
Subnetting
The IP Packet format
Packet Forwarding
Internet Control Message Protocol (ICMP)
Discovery protocols: ARP and DHCP
Turning names into addresses (DNS)

## Slide 3: Hop-by-Hop Packet Forwarding
Each router has a forwarding table
  Maps “network prefix” to an “outgoing interfaces”
Upon receiving a packet
  Inspect the destination IP address in the header
  Index into the table
  Determine the outgoing interface
  Forward the packet out that interface
Then, the next router in the path repeats
  And the packet travels along the path to the destination

## Slide 4: Packet Forwarding and Routing
The data plane and control plane are two components of network architecture, responsible for forwarding and managing network traffic.
Packet Forwarding (Data Plane)
  How to use Forwarding Tables
Packet Routing (Control Plane)
  How to populate Forwarding Tables (create routes)  Next lecture

## Slide 5: Inside a Router
Link 1, ingress
Link 1, egress
Link 2, ingress
Link 2, egress
Link 3, ingress
Link 3, egress
Link 4, ingress
Link 4, egress
Choose
Egress
Choose
Egress
Choose
Egress
Forwarding
Decision
Forwarding
Table

## Slide 6: Forwarding in an IP Router
When router receives a packet: it Looks for the network prefix in forwarding table that matches the destination address of the packet.
  If unknown, drops packet and send back error message if required.
  If known, it forwards it to the next-hop on the correct port.
    It first decrements TTL, and updates header Checksum.
    Then, IP asks the link layer on the outgoing interface to send the packet to the next-hop.
    The link layer will add proper header to the packet to create frame.
      The frame’s source MAC address will be the interface’s MAC address.
      The destination MAC address will be the next-hop’s MAC address.
Note: router doesn’t change source and destination IP address. Why?
Question:
  How is the address looked up in a real router?

## Slide 7: CIDR Makes Packet Forwarding Harder
Forwarding table may have many matches
  Assume a packet destined to 128.100.20.20 comes at Provider 1
128.0.0.0/8
128.100.17.0/24
128.100.18.0/24
128.100.19.0/24
128.100.20.0/24
Provider 2
Provider 1
R2
R1
IF2
Prefix | IF
128.100.0.0/16 | IF1
128.200.10.0/24 | IF1
128.1.0.0/16 | IF1
128.100.20.0/24 | IF2
R1’s Forwarding Table
IF3
IF4
IF5
IF1
IF1
IF2
128.100.20.20
?

## Slide 8: Longest Prefix Match Forwarding
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
128.0.0.0/8
128.100.17.0/24
128.100.18.0/24
128.100.19.0/24
128.100.20.0/24
Provider 2
Provider 1
R2
R1
IF2
Prefix | IF
128.100.0.0/16 | IF1
128.200.10.0/24 | IF1
128.1.0.0/16 | IF1
128.100.20.0/24 | IF2
R1’s Forwarding Table
IF3
IF4
IF5
IF1
IF1
IF2
128.100.20.20

## Slide 9: Simplest Algorithm is Too Slow
Scan the forwarding table one entry at a time
  See if the destination matches the entry
  If so, check the size of the mask for the prefix
  Keep track of the entry with longest-matching prefix
Overhead is linear in size of the forwarding table
  Today, that means 400,000-500,000 entries!
  The router have just a few nanoseconds before the next packet arrives
Need greater efficiency to keep up with line rate
  Better algorithms
  Hardware implementations

## Slide 10: Fast Lookups
There are algorithms that are faster than linear scan
  Proportional to number of bits in the address
We can use special hardware
  Content Addressable Memories (CAMs)
  Allows look-ups on a key rather than flat address
Huge innovations in the mid-to-late 1990s
  CIDR was introduced in 1994, and longest-prefix match was a major bottleneck then

## Slide 11: Where do Forwarding Tables Come From?
Forwarding table entries can be statically configured
  e.g., “map 12.34.158.0/24 to Serial0/0.1”
However, this doesn’t adapt to
  Failures, new equipment, the need to balance load, etc.
That is where other protocols come in …
  Routing protocols  Next week