## Slide 1: CSC358: Principles of Computer Networks
Lecture 6 – Part 6: DHCP and ARP
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: Today
IP Addressing
Subnetting
The IP Packet format
Packet Forwarding
Internet Control Message Protocol (ICMP)
Discovery protocols: ARP and DHCP
Turning names into addresses (DNS)
ARP
DHCP
Network

## Slide 3: What Happens at The Link Layer?
What does it mean to send to IF1?
Prefix | IF/Next hop
1.2.1.0/24 | IF1
1.2.2.0/24 | IF2
8.0.0.0/30 | IF0
Default | 8.0.0.2
1.2.1.3
1.2.2.100
1.2.1.1
1.2.2.1
IF1
IF2
IF0

## Slide 4: Discovery
Suppose I am host A and I want to communicate with B (say, www.google.com)
I was “born” knowing only my name – my MAC address
Must discover some information before I can communicate with B
  What is my IP address?
  What is B’s IP address?
    Using DNS
  Is B within my LAN?
  If yes, what is B’s MAC address?
  If not, what is the address of my first-hop router to B?
  …

## Slide 5: DHCP and ARP
Discovery protocols
  DHCP – Dynamic Host Configuration Protocol
  ARP – Address Resolution Protocol
Configured to a single LAN
Rely on broadcast capability

## Slide 6: DHCP and ARP
Serve two functions
  By DHCP: Bootstrap communication with remote hosts
    What’s my IP address?
    What’s my subnet masks? Allows to test whether an IP address is local or not
    What’s the IP address(es) for my local DNS name server(s)
    What’s the IP address(es) for my first-hop “default” router(s)
  By ARP: Discovery of local end-hosts
    For communication between hosts on the same LAN

## Slide 7: DHCP: Operation
Dynamic Host Configuration Protocol
  Defined in RFC 2131
One or more local DHCP servers maintain required information
  IP address pool, netmask, DNS servers, etc.
  Application that listens on UDP port 67

## Slide 8: DHCP: Operation
Dynamic Host Configuration Protocol
  Defined in RFC 2131
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
  L2 broadcast, to MAC address ff:ff:ff:ff:ff:ff

## Slide 9: DHCP: Operation
Dynamic Host Configuration Protocol
  Defined in RFC 2131
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers respond with a DHCP “offer” message
  Proposed IP address for client, lease time
  Other parameters

## Slide 10: DHCP: Operation
Dynamic Host Configuration Protocol
  Defined in RFC 2131
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers respond with a DHCP “offer” message
Client broadcasts a DHCP request message
  Specifies which offer it wants
  Echoes accepted parameters
  Other DHCP servers learn they were not chosen

## Slide 11: DHCP: Operation
Dynamic Host Configuration Protocol
  Defined in RFC 2131
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers respond with a DHCP “offer” message
Client broadcasts a DHCP request message
Selected DHCP server responds with an ACK

## Slide 12: Are We There Yet?

## Slide 13: ARP: Address Resolution Protocol
Every host maintains an ARP table
  List of (IP address – MAC address) pairs
  For IP addresses within the same LAN
Consult the table when sending a packet
  Map destination IP address to destination MAC address
But what if IP address not in table?
  Either its not local (detected using DHCP)
    So, send it to the router (i.e., destination MAC address is router’s MAC)
  If it’s local:
    Sender broadcasts: “Who has IP address 1.2.3.156?”
    The device with that IP address replies and report its MAC address.
    Caches the answer in ARP table