## Slide 1: CSC358: Principles of Computer Networks
Lecture 7 – Part 2a: Distance Vector
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: Today
Part 1: The Routing Concept & Algorithms
Part 2: Distance Vector (DV): Distributed Bellman Ford Algorithm
  Part 2.a: A DV that works
  Part 2.b: Adding more feature to optimize:
    Poison Expired Routes
    Split Horizon
    Poison Reverse
    Count To Infinity
Part 3: Link State (LS): Dijkstra’s Shortest Path First-based Algorithm

## Slide 3: Distance Vector (DV): Distributed Bellman-Ford Algorithm
Main Idea behind DV protocols:
  Routers “advertise” their best-known paths to their neighbors.
  Router update their best-known paths based on neighbors’ ads.
    Let dR(A) denote the best-known path from router R to network A
    dR1(A) = min {c(R1, X) + dX(A)} over all routers X that are neighbor to R1
For instance: dR1(A) = min{c(R1, R2) + dR2(A), c(R1, R3) + dR3(A)}
3
2
2
1
1
4
1
4
5
3
R2
R3
R6
R7
R8
R4
R5
R1
Cost of the edge connecting R1 to X
Cost of router X’s best-known path to network A
A
1

## Slide 4: DV Algorithm Key Ideas
c(x,v) = cost for direct link from x to v
  Node x maintains costs of direct links c(x,v)
Dx(y) = estimate of least cost from x to y
  Node x maintains distance vector Dx = [Dx(y): y є N ]
Node x maintains its neighbors’ distance vectors
  For each neighbor v, x maintains Dv = [Dv(y): y є N ]
Each node v periodically sends Dv to its neighbors
  And neighbors update their own distance vectors
  Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Over time, the distance vector Dx converges to the optimal value.

## Slide 5: Distance Vector Algorithm
Iterative, asynchronous, distributed
  Each local iteration caused by:
    Local link cost change
    Distance vector update message from neighbor
  Distributed:
    Each node notifies neighbors when its DV changes, and periodically
wait for (change in local link cost or message from neighbor)
recompute estimates
if DV to any destination has changed, notify neighbors.
Otherwise, send distance vector periodically.
Each router:

## Slide 6: DV Example: Step 0
No cost on edge means the cost is 1.
By the end of step 0: All Optimum 0-hop paths will be found.
Table for R1 |  | 
Dst | Cst | Hop
A | 1 | direct
Table for R2 |  | 
Dst | Cst | Hop
B | 1 | direct
Table for R3 |  | 
Dst | Cst | Hop
C | 1 | direct
Table for R4 |  | 
Dst | Cst | Hop
D | 1 | direct
Table for R5 |  | 
Dst | Cst | Hop
E | 1 | direct
Table for R6 |  | 
Dst | Cst | Hop
F | 1 | direct
R1
R5
R6
R3
R4
R2
2
3
6
4
3
A
E
C
D
B
F
R1 announces its distance vector to its neighbors:
  Notice: R1's announcement doesn't include the next-hop. Nobody else cares how R1 reaches A.
R1 Distance Vector | 
Dst. | Cst
A | 1

## Slide 7: Distance Vector Example: Step 1
All Optimum 1-hop paths will be found by the end of step 1.
Table for R1 |  | 
Dst | Cst | Hop
A | 1 | direct
B | 5 | R2
E | 3 | R5
F | 7 | R6
Table for R2 |  | 
Dst | Cst | Hop
A | 5 | R1
B | 1 | direct
D | 4 | R4
F | 2 | R6
Table for R3 |  | 
Dst | Cst | Hop
C | 1 | direct
D | 2 | R4
F | 2 | R6
Table for R4 |  | 
Dst | Cst | Hop
B | 4 | R2
C | 2 | R3
D | 1 | direct
Table for R5 |  | 
Dst | Cst | Hop
A | 3 | R1
E | 1 | direct
F | 4 | R6
Table for R6 |  | 
Dst | Cst | Hop
A | 7 | R1
B | 2 | R2
C | 2 | R3
E | 4 | R5
F | 1 | direct
R1
R5
R6
R3
R4
R2
2
3
6
4
3
A
E
C
D
B
F
All routers’ tables are updated. So, all of them announce their distance vectors to their neighbors.

## Slide 8: Distance Vector Example: Step 2
All Optimum 2-hop paths will be found by the end of step 2.
Table for R1 |  | 
Dst | Cst | Hop
A | 1 | direct
B | 5 | B
C | 8 | F
D | 8 | B
E | 3 | E
F | 6 | E
Table for R2 |  | 
Dst | Cst | Hop
A | 5 | A
B | 1 | direct
C | 3 | F
D | 4 | D
E | 5 | F
F | 2 | F
Table for R3 |  | 
Dst | Cst | Hop
A | 8 | F
B | 3 | F
C | 1 | direct
D | 2 | D
E | 5 | F
F | 2 | F
Table for R4 |  | 
Dst | Cst | Hop
A | 8 | B
B | 4 | B
C | 2 | C
D | 1 | direct
F | 3 | C
Table for R5 |  | 
Dst | Cst | Hop
A | 3 | A
B | 5 | F
C | 5 | F
E | 1 | direct
F | 4 | F
Table for R6 |  | 
Dst | Cst | Hop
A | 6 | B
B | 2 | B
C | 2 | C
D | 3 | C
E | 4 | E
F | 1 | direct
R1
R5
R6
R3
R4
R2
2
3
6
4
3
A
E
C
D
B
F

## Slide 9: Distance Vector Example: Step 3
All Optimum 3-hop paths will be found by the end of step 3.
R1
R5
R6
R3
R4
R2
2
3
6
4
3
Table for R1 |  | 
Dst | Cst | Hop
A | 1 | direct
B | 5 | R2
C | 7 | R5
D | 8 | R2
E | 3 | R5
F | 6 | R5
Table for R2 |  | 
Dst | Cst | Hop
A | 5 | R1
B | 1 | direct
C | 3 | R6
D | 4 | R4
E | 5 | R6
F | 2 | R6
Table for R3 |  | 
Dst | Cst | Hop
A | 7 | R6
B | 3 | R6
C | 1 | direct
D | 2 | R4
E | 5 | R6
F | 2 | R6
Table for R4 |  | 
Dst | Cst | Hop
A | 8 | R2
B | 4 | R2
C | 2 | R3
D | 1 | direct
E | 6 | R3
F | 3 | R3
Table for R5 |  | 
Dst | Cst | Hop
A | 3 | R1
B | 5 | R6
C | 5 | R6
D | 6 | R6
E | 1 | R5
F | 4 | R6
Table for R6 |  | 
Dst | Cst | Hop
A | 6 | R2
B | 2 | R2
C | 2 | R3
D | 3 | R3
E | 4 | R5
F | 1 | R6
A
E
C
D
B
F

## Slide 10: A Deeper Look Into The DV Algorithm
For each destination:
  If you hear an advertisement, update table and reset TTL if:
    The destination isn't in the table. (#1)
    Advertised cost + link cost to neighbor < best-known cost (#2)
    The advertisement is from current next-hop (#3)
  Advertise to all your neighbors when the table updates, and periodically (#4)
  If a table entry expires, delete it (#5)
In previous example, we saw (#1) and (#2). But why do we need (#3), (#4), and (#5)?

## Slide 11: Why Do We Need (#3)?
So far: We update if we get a better path (or if we didn't have a path before), i.e., #1 and (#2).
R3
R1
R2
R3's Table |  | 
To: | Via: | Cost:
R3's Table |  | 
Dst | Hop | Cost
A | R2 | 1+3 = 4
I'm R2, and A is 3 away from me.
A wasn't in my table. Accept!
1
1
R2’s DV | 
Dst | Cost
A | 3
R2’s DV | 
Dst | Cost
A | 3
In the upcoming cartoons, we show the advertisement in an abstract (conceptual) way. In reality, Routers do not send a message saying “I'm R2, and A is 3 away from me.” As we discussed, they send their distance vector, i.e.,

## Slide 12: Why Do We Need (#3)?
So far: We update if we get a better path (or if we didn't have a path before), i.e., #1 and (#2).
R3
R1
R2
R3's Table |  | 
Dst | Hop | Cost:
A | R2 | 4
I'm R1, and A is 8 away from me.
1+8=9 is worse than 4.
Reject!

## Slide 13: Why Do We Need (#3)?
Recall that the network topology can change.
  (#3) lets the next-hop notify us if the topology changed.
R3
R1
R2
I'm R2, and A is 8 away from me.
R2 is the next-hop. Accept!
R3's Table |  | 
To: | Via: | Cost:
A | R2 | 4
R3's Table |  | 
Dst | Hop | Cost:
A | R2 | 1+8=9
Hi, it's R2 again. I know I said A is 3 away from me earlier, but that's changed. Now A is 8 away.
What R2 is really saying:

## Slide 14: Why Do We Need (#4)?
For each destination:
  If you hear an advertisement, update table and reset TTL if:
    The destination isn't in the table. (#1)
    Advertised cost + link cost to neighbor < best-known cost. (#2)
    The advertisement is from current next-hop. (#3)
  Advertise to all your neighbors when the table updates, and periodically. (#4)
  If a table entry expires, delete it. (#5)
Why do we need to send periodically in (#4)?
  Recall that packets can get dropped, including advertisements.
    So, we send advertisement every X seconds. Thus, eventually the advertisement will be received.

## Slide 15: Why Do We Need (#5)?
For each destination:
  If you hear an advertisement, update table and reset TTL if:
    The destination isn't in the table. (#1)
    Advertised cost + link cost to neighbor < best-known cost. (#2)
    The advertisement is from current next-hop. (#3)
  Advertise to all your neighbors when the table updates, and periodically. (#4)
  If a table entry expires, delete it. (#5)
Why do we need (#5)?

## Slide 16: Why Expiry in (#5)?
Recall that links and routers can fail.
  Periodic advertisements help us confirm that a route still exists.
    When we get an advertisement, reset ("recharge") the TTL.
  If a link goes down, we stop getting periodic updates, and the TTL will expire.
    If the TTL expires, delete the entry from the table.
R3
R2
Didn't have a path to A. Accept!
R3's Table |  |  | 
To: | Via: | Cost: | TTL:
At t=0:
I'm R2, and A is 5 away from me.
R3's Table |  |  | 
To: | Via: | Cost: | TTL:
A | R2 | 6 | 11
t = 0
Need another confirmation of this route in the next 11 seconds.
A

## Slide 17: Why Expiry in (#5)?
Recall that links and routers can fail.
  Periodic advertisements help us confirm that a route still exists.
    When we get an advertisement, reset ("recharge") the TTL.
  If a link goes down, we stop getting periodic updates, and the TTL will expire.
    If the TTL expires, delete the entry from the table.
R3's Table |  |  | 
To: | Via: | Cost: | TTL:
A | R2 | 6 | 7
t = 4
R3
R2
A

## Slide 18: Why Expiry in (#5)?
Recall that links and routers can fail.
  Periodic advertisements help us confirm that a route still exists.
    When we get an advertisement, reset ("recharge") the TTL.
  If a link goes down, we stop getting periodic updates, and the TTL will expire.
    If the TTL expires, delete the entry from the table.
R3's Table |  |  | 
To: | Via: | Cost: | TTL:
A | R2 | 6 | 11
t = 5
We got a confirmation! Reset TTL back to 11.
At t=5:
I'm still R2, and A is still 5 away from me.
R3
R2
A

## Slide 19: Why Expiry in (#5)?
Recall that links and routers can fail.
  Periodic advertisements help us confirm that a route still exists.
    When we get an advertisement, reset ("recharge") the TTL.
  If a link goes down, we stop getting periodic updates, and the TTL will expire.
    If the TTL expires, delete the entry from the table.
R3's Table |  |  | 
To: | Via: | Cost: | TTL:
A | R2 | 6 | 10
t = 6
At t=6:
This link goes down
R3
R2
A

## Slide 20: Why Expiry in (#5)?
Recall that links and routers can fail.
  Periodic advertisements help us confirm that a route still exists.
    When we get an advertisement, reset ("recharge") the TTL.
  If a link goes down, we stop getting periodic updates, and the TTL will expire.
    If the TTL expires, delete the entry from the table.
R3
R2
A
R3's Table |  |  | 
To: | Via: | Cost: | TTL:
A | R2 | 6 | 0
t = 16
Timeout! Delete expired entry.

## Slide 21: We have a Functional DV!
For each destination:
  If you hear an advertisement, update table and reset TTL if:
    The destination isn't in the table. (#1)
    Advertised cost + link cost to neighbor < best-known cost. (#2)
    The advertisement is from current next-hop. (#3)
  Advertise to all your neighbors when the table updates, and periodically. (#4)
  If a table entry expires, delete it. (#5)
This is a mostly-functional protocol now. However, we can do better. We’ll add some optimizations for faster convergence.