## Slide 1: CSC358: Principles of Computer Networks
Lecture 8 – Part 4: Joining BGP and IGP; BGP details
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: Today
Part 1: Routing Techniques, cont’d
  Link state routing protocol
Part 2:
  Intra-domain vs. Inter-domain Routing
  Business relationship among ASes
Part 3:
  BGP vs. DV
  Gao-Rexford Rules for Selecting and Exporting Path
Part 4:
  Joining BGP and IGP Information
  BGP protocol details

## Slide 3: Combining Intra-Domain and Inter-Domain Routing
AS4
AS1
AS2
AS3
AS5
So far, we've shown BGP in terms of ASes talking to each other.

## Slide 4: Combining Intra-Domain and Inter-Domain Routing
AS1
AS2
AS3
AS5
Border router
Internal router
In reality, an AS is made up of a bunch of routers.
  Border routers and Internal Routers
We have to ensure the routers "act as one."

## Slide 5: Who Speaks BGP? Border routers at an AS
AS1
AS2
AS3
AS5
BGP speakers: The routers that advertise BGP paths to other ASes.
  Speakers must understand BGP syntax and semantics.
Who speaks BGP? All the border routers inside each AS.

## Slide 6: BGP “sessions”, eBGP session and iBGP session
A border router uses eBGP session to exchange inter-domain routes
with border routers in other ASes through
“eBGP session”
Hi neighbor. You can reach Z via me.

## Slide 7: BGP “sessions”, eBGP session and iBGP session
A border router uses iBGP to distribute the routes it discovers to everyone
else in the AS (i.e., interior and border routers in its own AS)
“iBGP session”
Hi routers in my AS. You can reach Z via me.

## Slide 8: eBGP, iBGP, and IGP
eBGP: BGP sessions between border routers in different ASes
  Learn routes to external destinations
iBGP: BGP sessions between border routers and other routers within the same AS
  Distribute externally learned routes internally
IGP: “Interior Gateway Protocol” = Intra-domain routing protocol
  Provide internal reachability
  e.g., Link State Protocols like OSPF and IS-IS, and Distance Vector Protocols like RIP
Be careful not to confuse iBGP and IGP.
  Both are between interior routers.
  iBGP is for external routes, and IGP is for internal routes.

## Slide 9: Putting the Pieces Together
Provide internal reachability (IGP)
Learn routes to external destinations (eBGP)
Distribute externally learned routes internally (iBGP)
Travel shortest path to egress (IGP)
An egress router for a destination is a border router who can reach that destination.
6
2
4
9
2
1
3
3
z

## Slide 10: Joining BGP and IGP Information
A’s Combined Table
A’s IGP Table
AS 7
AS 88
192.0.2.1
10.10.10.10
A’s BGP Table
192.0.2.1
128.112.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
destination
next hop
Reach 128.112.0.0/16
via 192.0.2.1
128.112.0.0/16
destination
next hop
10.10.10.10
+
192.0.2.0/30
10.10.10.10
E
B
A
128.112.0.0/16
Reach 128.112.0.0/16
via me.

## Slide 11: Today
Part 1: Routing Techniques, cont’d
  Link state routing protocol
Part 2:
  Intra-domain vs. Inter-domain Routing
  Business relationship among ASes
Part 3:
  BGP vs. DV
  Gao-Rexford Rules for Selecting and Exporting Path
Part 4:
  Joining BGP and IGP Information
  BGP protocol details

## Slide 12: Basic Messages in BGP
Open Messages
  Establishes BGP session
  BGP uses TCP [will talk about TCP in 1-2 weeks]
Notification Messages
  Report unusual conditions
Update Messages
  Inform neighbor of new routes
  Inform neighbor of old routes that become inactive
Keepalive Messages
  Inform neighbor that connection is still viable

## Slide 13: Update Messages
Two kinds of updates
  Announcements: new routes or changes to existing routes
  Withdrawal: remove routes that no longer exist
Format of Announcement messages: <IP prefix: route attributes>
  Attributes describe properties of the route and are used in route selection and export decisions.
  Some attributes are public, i.e., included in eBGP route announcements.
  And some are local, i.e., private within an AS, not included in eBGP route announcements.
  There are many standardized attributes in BGP. We will discuss three of them: ASPATH, MED, and IGP COST

## Slide 14: Attributes (1): ASPATH
Carried in eBGP route announcements
It’s a vector that lists all the ASes a route advertisement has traversed (in reverse order)
AS 577
Bell Canada
AS 12654
IP prefix = 128.100.0.0/16
AS path = (577, 239)
AS 239
UofT, 128.100/16
IP prefix = 128.100.0.0/16
AS path = (239)

## Slide 15: Attributes (2): IGP cost
Used for hot-potato routing
  Each router selects the closest egress point based on the path cost in intra-domain protocol
Verizon
A
B
E
F
G
C
H
D
I
AT&T
X
Y
[eBGP] I can reach Y.
[eBGP] I can reach Y.
[iBGP] Hi everyone, I have a path to Y.
[iBGP] Hi everyone, I have a path to Y.
I and F can both reach Y using the same AS path.
I'll use F to exit since it's closer.

## Slide 16: Attributes (3): MED
“Multi-Exit Discriminator”
Used when ASes are interconnected via 2 or more links
  to specify how close a prefix is to the link it is announced on
AS announcing prefix sets MED
AS receiving prefix (optionally!) uses MED to select link
  Smaller MED is better
Verizon
B
C
F
G
H
D
I
E
J
AT&T
X
Y
A
F and J are equally far away.
I'll use J, since it's got a lower MED.
[eBGP] I can reach Y. It's 5 away from me.
[eBGP] I can reach Y. It's 1 away from me.
[iBGP] Hi everyone, I have a path to Y.
The other AS said this path has MED=5.
[iBGP] Hi everyone, I have a path to Y.
The other AS said this path has MED=1.

## Slide 17: Use Attributes to Implement Typical Selection Policy
Selecting rules:
  Use Gao-Rexford Rules: Make/save money (send to customer > peer > provider)
  If 1 tied, maximize performance (smallest AS path length)
  If 1-2 tied, minimize use of my network bandwidth (“hot potato”)
  If 1-3 tied, Lowest MED preferred
Exporting rules:
  Use Gao-Rexford rules to decide which ASes hear about this route.
  In the announcement, include the MED (distance from router to destination). Lower MED = Prefer to use this router.

## Slide 18: BGP UPDATE Processing
Best Route
Selection
Apply Import
Policies
Best Route
Table
Apply Export
Policies
forwarding
Entries
BGP
Updates
BGP
Updates
IP Forwarding Table
Constrained only by vendor configuration language
Data plane
Control plane
Data packets
Data packets