## Slide 1: CSC358: Principles of Computer Networks
Lecture 9 – Part 1: Putting Things Together
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: Today’s Outline
Part 1:
  Putting Things Together (review)
Part 2:
  The Final Piece in the Game: Socket
Part 3:
  The Web and HTTP
    HTTP and improving its performance
      Pipelined, Persistent, Caching
Part 4:
  Transport Layer

## Slide 3: What does the Internet Actually Look Like?
The smallest component:
  A Network Interface Card (NIC), or a machine, or a server
  Has a globally unique Link Layer MAC name/address
    48 bits
    Flat addressing scheme (i.e., no hierarchy)
Multiple NICs are connected in a Local Area Network (LAN) via
  Shared medium (e.g., 10BASE5 Ethernet) or switched network (e.g., Switched Ethernet)
    i.e., in a LAN, nodes are connected via Link layer functionalities, and no router is in between them.

## Slide 4: What does the Internet Actually Look Like?
LANs get connected to each other by routers
Each node gets an IP address
  32 bits
  Hierarchical addressing scheme (i.e., it is not flat)
  A device’s IP address is not necessarily globally unique (i.e., multiple may have the same IP address)

## Slide 5: What does the Internet Actually Look Like?
A collection of local networks that are under a single administrative control is an AS.
ASes get connected to each other by routers
  More precisely, by border routers
Each AS is assigned a unique 32-bit address
  Flat addressing scheme (i.e., no hierarchy)

## Slide 6: Navigating Packets in a LAN
How do we deliver packets in a switched LAN?
  Switches use flooding and MAC learning
    If you know the destination can be reached through a port, then use it
    Otherwise, send out the frame on all ports (i.e., flooding)
      Flooding guarantees that the destination will receive the frame.
  Switches do not share their forwarding tables or network topology with each other.
How do we take care of loops in a switched LAN?
  Since we use flooding, loops can lead to disaster
  Thus, we use STP and deactivate some links to get rid of loops
How do we deliver packets in a shared medium LAN?
  Medium Access Control techniques (e.g., CSMA/CD)

## Slide 7: Navigating Packets in an AS (i.e., Intra-domain)
How do routers deliver packets in an AS?
  Routers find the least-cost path
    If you know which port connects you to the least-cost path, then it use it
    Otherwise, drop the packet (i.e., NO flooding)
  Depending on the intra-domain routing protocol, routers share the information from their forwarding tables (e.g., Distance Vector) or network topology (e.g., Link States) with each other.
Routers don’t use flooding, so we don’t need to worry about loops anymore?
  NO! Invalid global routing state may lead to a packet get stuck in a loop and never get delivered (e.g., )
How do we take care of loops in an AS?
  Routers use least-cost paths. Furthermore, all routers must use the same cost metric and the same tie breaking rule.
  This results in having no loops in the global routing state.

## Slide 8: Navigating Packets Across ASes (i.e., Inter-domain)
How do routers deliver packets from one AS to another?
  Routers don’t use least-cost path for inter-domain routing.
  Instead, they use their own AS policy to choose a route.
  Each AS can have its own strange policy.
Now that we don’t use least-cost paths, how can we handle loops?
  BGP speaking routers share the path vector with each other.
  Whenever you receive an advertisement, look inside the path vector.
    If by adding yourself to the path you will cause a loop, then don’t use the advertised path.

## Slide 9: Networks and Routers

## Slide 10: Types of Routers
Router’s capacity is defined as Speed (“line rate”) of each port no. of ports
Core: Cisco CRS
  line rate = 10/40/100 Gbps
  capacity = 922 Tbps
  Netflix: 0.7 GB/hr (1.5Mb/s)
  ~600 million concurrent Netflix users
Edge (ISP): Cisco ASR
  Speed (“line rate”) of each port = 1/10/40 Gbps
  capacity = 120 Gbps
Edge (enterprise): Cisco 3945E
  line rate = 10/100/1000 Mbps
  capacity < 10 Gbps

## Slide 11: How does Internet Work? End-to-end Perspective
Network stack receives data from the application (roughly speaking)
What is my IP address? (DHCP has the answer)
What is the destination IP address? (use DNS)
Encapsulate data into packets (and add an IP header)
Is destination IP address within my LAN? (use the information from DHCP)
  What should the host do if the destination address is local?
  What should it do if the destination address is remote?

## Slide 12: How does Internet Work? End-host Perspective
If destination IP address is local:
  What is destination MAC address (use ARP)?
  Encapsulate packet into frames (and add a Link layer header)
  Convert frames into bits and signal
  Forward the bits to the wire (i.e., send the signal)
  Switches will take care of the rest …

## Slide 13: How does Internet Work? End-host Perspective
If destination IP address is remote:
  What is my next-hop router IP address? (DHCP has the answer)
  What is my next-hop router MAC address? (use ARP)
  Encapsulate packet into frames (and add a Link layer header)
  Convert frames into bits and signal
  Forward the bits to the wire (i.e., send the signal)
  Routers will take care of the rest …