## Slide 1: CSC358: Principles of Computer Networks
Lecture 10 – Part 6: Other TCP Mechanisms
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: Today’s Lecture
Part 4: Principles of congestion control
Part 5: TCP congestion control
Part 6: Other TCP mechanisms
  Nagle’s algorithm and delayed acknowledgments
Part 7: Network Address Translation (NAT)
Important note: This part, i.e., part 6 will not be covered on your final exam

## Slide 3: Motivation for Nagle’s Algorithm
Interactive applications like Telnet, ssh and rlogin generate many small packets (e.g., keystrokes)
Small packets are wasteful
  Mostly header (e.g., 40 bytes of header, 1 byte of data)
It’s tempting to reduce the number of packets by forcing every packet to have some minimum size
  But, what if the person doesn’t type more characters?
Thus, we need to balance competing trade-offs
  i.e., send larger packets but don’t introduce much delay by waiting.

## Slide 4: Nagle’s Algorithm
Wait if the amount of data is applications and some other packet is already in flight
  i.e., the amount of data waiting to be sent is smaller than Maximum Segment Size (MSS)
  And still awaiting the ACKs for previous packets
By waiting until all outstanding ACKs have arrived, we ensure that we send at most one small packet per RTT
What’s the Influence of Nagle’s algorithm on performance?
  Improves the performance for interactive applications: enables batching of bytes
  No impact on bulk transfer: transmits in MSS-sized packets anyway
vs.
ACK

## Slide 5: Motivation for Delayed ACK
TCP traffic is often bidirectional
  Data traveling in both directions
  ACKs traveling in both directions
ACK packets have high overhead
  40 bytes for the IP header and TCP header and zero data traffic
Piggybacking is appealing
  Host B can send an ACK to host A
  … as part of a data packet from B to A

## Slide 6: TCP Header Allows Piggybacking
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Flags:
SYN
FIN
RST
PSH
URG
ACK

## Slide 7: Example of Piggybacking
Data
Data+ACK
Data
A
B
ACK
Data
Data + ACK
B has data to send
A has data to send
B doesn’t have data to send

## Slide 8: Increasing Likelihood of Piggybacking
Increase likelihood of piggybacking
  TCP allows the receiver to wait to send the ACK
  … in the hope that the host will have data to send
Example: rlogin or telnet
  Host A types characters at a UNIX prompt
  Host B receives the character and executes a command
  … and then data are generated
  Would be nice if B could send the ACK with the new data
Data
Data+ACK
Data
A
B
ACK
Data
Data + ACK

## Slide 9: Delayed ACK
Delay sending an ACK
  Upon receiving a packet, the host B sets a timer
    Typically, 200 msec or 500 msec
  If B’s application generates data, go ahead and send
    And piggyback the ACK bit
  If the timer expires, send a (non-piggybacked) ACK