## Slide 1: CSC358: Principles of Computer Networks
Lecture 10 – Part 7: NAT
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: History of NATs
IP address space depletion
  Clear in early 90s that 232 addresses not enough
  Work began on a successor to IPv4
In the meantime…
  Share addresses among numerous devices
  … without requiring changes to existing hosts
Meant to provide temporary relief
  Intended as a short-term remedy
  Now, NAT are very widely deployed
  … much more so than IPv6

## Slide 3: NAT is an Active Component in the Data Path
NAT
inside
outside

## Slide 4: NAT Translates IP Header
NAT stands for network address translation.
It’s a way to map multiple private IP addresses inside a local network to a public IP address before transferring the information onto the internet.
But, what are Private IP Addresses?

## Slide 5: What are Private IP Addresses?
RFC-1918 defines private IPv4 address ranges reserved by the IANA for private networks, which are not publicly routable on the global internet. The reserved ranges are:
  10.0.0.0/8 IP addresses: 10.0.0.0 – 10.255.255.255
  172.16.0.0/12 IP addresses: 172.16.0.0 – 172.31.255.255
  192.168.0.0/16 IP addresses: 192.168.0.0 – 192.168.255.255
Unlike public IP addresses, Enterprises can use these Private address spaces without coordination with IANA or an Internet registry.
Public IP addresses must be globally unique. Private IP addresses must be unique only within the enterprise.

## Slide 6: NAT Translates IP Header, cont’d
Organizations that want multiple devices to employ a single IP address use NAT, as do most home routers.
  your cable modem or DSL router usually provide NAT to your home.
In a nutshell, NAT rewrites the IP addresses
  It makes the “inside” look like a single IP address.
  Since it changes the IP header, it must update header checksums, as well.
  For outbound traffic, i.e., traffic from inside to outside:
    NAT rewrites the source IP address
  For inbound traffic, i.e., traffic from outside to inside:
    NAT rewrites the destination IP address

## Slide 7: Using a Single Source Address
NAT
inside
outside
10.0.0.1
10.0.0.2
138.76.29.7

## Slide 8: NATs Challenges
NAT gives packets same source address
  All packets have source address 138.76.29.7
Problems:
  How can the destination differentiate between senders?
  How can the destination return traffic get back to the correct hosts?

## Slide 9: Port-Translating NAT
Map outgoing packets
  Replace source address with NATs public IP address
  Replace source port number with a new port number
  Remote hosts respond using (NATs public IP address, new port #)
Maintain a translation table
  Store map of (source IP address, port #) to (NAT public IP address, new port #)
Map incoming packets
  Consult the translation table
  Map the destination address and port number
  Local host receives the incoming packet

## Slide 10: Network Address Translation Example
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 11: Maintaining the Mapping Table
Create an entry upon seeing a packet
  Packet with new (source IP addr, source port) pair
Eventually, need to delete the map entry. But when to remove the binding?
  If no packets arrive within a time window, then delete the mapping to free up the port #s
  This is another example of “soft state”, i.e., removing state if not refreshed for a while

## Slide 12: Objections Against NAT
Port #s are meant for addressing processes
  Yet, NAT uses them to identify end hosts
  Makes it hard to run a server behind a NAT
NAT
10.0.0.1
10.0.0.2
138.76.29.7
Requests to 138.76.29.7 on port 80
Which host should get the request???

## Slide 13: Objections Against NAT
Difficult to support peer-to-peer applications
  P2P needs a host to act as a server
  … difficult if both hosts are behind NATs
Routers are not supposed to look at port #s
  Network layer should care only about IP header
  … and not be looking at the port numbers at all
NAT violates the end-to-end argument
  Network nodes should not modify the packets
IPv6 is a cleaner solution
  Better to migrate than to limp along with a hack

## Slide 14: Where is NAT Implemented?
Home router (e.g., Linksys box)
  Integrates router, DHCP server, NAT, etc.
  Use single IP address from the ISP and have a bunch of hosts hiding behind it
Campus or corporate network
  NAT at the connection to the Internet
  Share a collection of public IP addresses
  Avoid complexity of renumbering end hosts and local routers when changing service providers